## Slide 1: Computational Intelligence (TC2027)

## Slide 2: Unit 2 – Network Review
Goals
Numbers System
Review of Network Architectures
OSI & TCP/ Reference Model
IP Protocol
ARP / RARP
ICMP

## Slide 3: Attention!!!!
It is not an introduction course; it is a review course.
It is expected that students have background in the networking and operational system.

## Slide 4: Numbers System

## Slide 5: Data Representation
Humans use decimal (base 10) numbers to represent numeric information, and various alphabets and symbol systems to represent other types of information.
In contrast, computers understand only one basic type of information: ones and zeroes, which themselves are representative of either an “on” or “off” electrical or light state within the hardware of the device.
  For this reason, larger collections of bits have been defined by computer scientists, such as bytes (octets), words, and so forth.

## Slide 6: Binary to Decimal Conversion

## Slide 7: Decimal to Binary Conversion

## Slide 8: Hexadecimal Number System

## Slide 9: Hexadecimal Number System

## Slide 10: Review of Network Architectures

## Slide 11: Types of Network

## Slide 12: Network Topologies

## Slide 13: OSI & TCP/ Reference Model

## Slide 14: ISO/OSI Model
OSI or Open System Interconnection model was developed by International Standards Organization (ISO).
It gives a layered networking framework that conceptualizes how communications should be done between heterogeneous systems.
The focus was to provide interoperability between providers (temporal context -> computer, networks and appliance were provided by the same company).

## Slide 15: TCP/IP Architecture

## Slide 17: TCP/IP x ISO/OSI Model

## Slide 18: TCP/IP Architecture
Data Encapsulation
Hunt, C. (2002). TCP/IP network administration (Vol. 2). " O'Reilly Media, Inc.".

## Slide 19: TCP/IP Architecture
Data Structure
Hunt, C. (2002). TCP/IP network administration (Vol. 2). " O'Reilly Media, Inc.".

## Slide 20: Flow Control
Flow Control = Sender does not flood the receiver, but maximizes throughput
Sender throttled until receiver grants permission
Methods: Stop and wait, Sliding window

## Slide 21: Error Control
Error Control: Deliver frames without error, in the proper order to network layer
Error Detection: Cyclic Redundancy Check, Sequence Numbers, Ack/Nak, Time-out
Error Recovery: Automatic Repeat Request (ARQ) Stop and Wait, Go back n Selective Reject

## Slide 22: Connection-Oriented vs Connectionless
Connection-Oriented: Telephone System
  Path setup before data is sent
  Data need not have address. Circuit number is sufficient.
Connectionless: Postal System.
  Complete address on each packet
  The address decides the next hop at each router

## Slide 23: Network Medium Access
Collisions: some networks has a shared medium, so there are rules for sending packets of data to avoid conflicts and to protect data integrity. Nodes determine when the network is available for sending packets. It is possible that two or more nodes at different locations will attempt to send data at the same time. When this happens, a packet collision occurs.
  Minimizing collisions is a crucial element in the design and operation of networks.
  Increased collisions are often the result of too many users on the network. This leads to competition for network bandwidth and can slow the performance of the network from the user’s point of view.
  Segmenting the network is one way of reducing an overcrowded network, i.e., by dividing it into different pieces logically joined together with a bridge or switch.

## Slide 25: Network Interface Layer

## Slide 26: Ethernet Standard
Use the CSMA/CD

## Slide 27: IP Protocol

## Slide 28: Network Layer

## Slide 29: IEEE 802 Standards
IEEE 802 is a family of standards for LANs, which defines an LLC and several MAC sublayers

## Slide 30: IEEE 802.2/802.3

## Slide 31: Internet Layer

## Slide 32: Internet Protocol (IP)
The Internet Protocol is the heart of TCP/IP.
IP provides the basic packet delivery service on which TCP/IP networks are built.
Main Functions:
  Defining the datagram, which is the basic unit of transmission on the Internet
  Defining the Internet addressing scheme
  Moving data between the Network Access Layer and the Transport Layer
  Routing datagrams to remote hosts
  Performing fragmentation and re-assembly of datagrams

## Slide 33: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 34: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
  Too slow: 48GE ports and 4x10GE needs 176Gbps bandwidth DRAM: ~1-6 Gbps; TCAM is fast, but 400x cost of DRAM
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 35: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NEU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 36: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 37: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 38: Internet Protocol (IP)
Internet Header Length (IHL): Specifies the length of the IP header, in 32-bit words. This includes the length of any options fields and padding. The normal value of this field when no options are used is 5 (5 32-bit words = 5*4 = 20 bytes).
Type Of Service (TOS): A field designed to carry information to provide quality of service features (unused).
Total Length (TL): Length of header + data.
Limits packets to 65,535 bytes

## Slide 39: Internet Protocol (IP)
Identification: This field contains a 16-bit value that is a unique number for the original datagram.

## Slide 40: Internet Protocol (IP)
Flags:

## Slide 41: Internet Protocol (IP)
Fragment Offset: When fragmentation of a message occurs, this field specifies the offset, or position, in the overall message where the data in this fragment goes.
  It is specified in units of 8 bytes (64 bits). The first fragment has an offset of 0.

## Slide 42: Internet Protocol (IP)
Time To Live (TTL): Specifies how long the datagram is allowed to “live” on the network, in terms of router hops.
  Each router decrements the value of the TTL field (reduces it by one) prior to transmitting it.
  If the TTL field drops to zero, the datagram is assumed to have taken too long a route and is discarded.
Used to implement trace route

## Slide 43: Internet Protocol (IP)
Protocol:

## Slide 44: Internet Protocol (IP)
Header Checksum
Source and Destination Address
Options: One or more of several types of options may be included after the standard headers in certain IP datagrams.
Padding: If one or more options are included, and the number of bits used for them is not a multiple of 32, enough zero bits are added to “pad out” the header to a multiple of 32 bits (4 bytes).

## Slide 45: Problem: Fragmentation
Problem: each network has its own MTU
  DARPA principles: networks allowed to be heterogeneous
  Minimum MTU may not be known for a given path
IP Solution: fragmentation
  Split datagrams into pieces when MTU is reduced
  Reassemble original datagram at the receiver
MTU = 2000
MTU = 4000
MTU = 1500
Datagram
Dgram1
Dgram2
1
2
3
4

## Slide 46: Fragmentation Example
MTU = 2000
MTU = 4000
MTU = 1500
Data
Data
Data
IP Hdr
IP
IP
Length = 3820, M = 0
3800
20
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
1980
+ 1820
= 3800

## Slide 47: Fragmentation Example
MTU = 2000
MTU = 1500
Data
Data
IP
IP
Data
Data
IP
IP
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
20
20
1480
500
Length = 520, M = 1
Offset = 1480
Length = 1500, M = 1
Offset = 0
Data
Data
IP
IP
20
20
1480
340
Length = 360, M = 0
Offset = 3460
Length = 1500, M = 1
Offset = 1980
1480
+ 500
= 1980

## Slide 48: IP Message Reassembly Process
When a datagram is fragmented, either by the originating device or by one or more routers transmitting the datagram, it becomes multiple fragment datagrams.
The destination of the overall message must collect these fragments and then reassemble them into the original message.
Reassembly is accomplished by using the special information in the fields we saw in the preceding topic to help us “put the jigsaw puzzle back together again”.

## Slide 49: IP Fragment Reassembly
Performed at destination
M = 0 fragment gives us total data size
  360 – 20 + 3460 = 3800
Challenges:
  Out-of-order fragments
  Duplicate fragments
  Missing fragments
Basically, memory management nightmare
Data
IP
20
1480
Data
IP
20
500
Length = 520, M = 1, Offset = 1480
Length = 1500, M = 1, Offset = 0
Data
IP
20
1480
Data
IP
20
340
Length = 360, M = 0, Offset = 3460
Length = 1500, M = 1, Offset = 1980

## Slide 50: Fragmentation in Reality
Fragmentation is expensive
  Memory and CPU overhead for datagram reconstruction
  Want to avoid fragmentation if possible
MTU discovery protocol
  Send a packet with “don’t fragment” bit set
  Keep decreasing message length until one arrives
  May get “can’t fragment” error from a router, which will explicitly state the supported MTU
Router handling of fragments
  Fast, specialized hardware handles the common case
  Dedicated, general purpose CPU just for handling fragments

## Slide 51: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 52: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
  Too slow: 48GE ports and 4x10GE needs 176Gbps bandwidth DRAM: ~1-6 Gbps; TCAM is fast, but 400x cost of DRAM
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 53: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NEU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 54: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:
Based on slides from D. Choffnes Northeastern U. Revised Fall 2014 by P. Gill

## Slide 55: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 56: Internet Layer

## Slide 57: Address Resolution Protocol (ARP)

## Slide 58: (Reverse) Address Resolution Protocol (RARP/ARP)
The ARP and RARP protocols perform the translation between IP addresses and MAC layer addresses
  The Internet is based on IP addresses
  Data link protocols (Ethernet, FDDI, ATM) may have different (MAC) addresses

## Slide 59: How an address is translated?

## Slide 60: How does ARP work?

## Slide 61: ARP Package

## Slide 62: ARP Package

## Slide 63: ARP Example
PS: CRC, Preamble and SFD are part of the Ethernet frame.

## Slide 64: Internet Layer

## Slide 65: Internet Control Message Protocol (ICMP)
The Internet Control Message Protocol (ICMP) is a helper protocol that supports IP with facility for
  Error reporting
  Simple queries
ICMP messages are encapsulated as IP datagrams:

## Slide 66: ICMP message format
4 byte header:
Type (1 byte): type of ICMP message
Code (1 byte): subtype of ICMP message
Checksum (2 bytes): like IP header checksum. Checksum is calculated over entire ICMP message
If there is no additional data, there are 4 bytes set to zero.  each ICMP messages is at least 8 bytes long

## Slide 67: ICMP Query message
ICMP query:
Request sent by host to a router or host
Reply sent back to querying host

## Slide 68: ICMP Error message
ICMP error messages report error conditions
Typically sent when a datagram is discarded
Error message is often passed from ICMP to the application program

## Slide 69: Transport Layer

## Slide 70: Internet Transport Protocol
Provide logical communication between application processes running on different hosts
Run on end hosts
  Sender: breaks application messages into segments, and passes to network layer
  Receiver: reassembles segments into messages, passes to application layer
Multiple transport protocol available to applications
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 71: Unreliable Message Delivery Service
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
User Datagram Protocol (UDP)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents
SRC port
DST port
checksum
length
DATA

## Slide 72: Transmission Control Protocol (TCP)
Connection oriented
  Explicit set-up and tear-down of TCP session
Stream-of-bytes service
  Sends and receives a stream of bytes, not messages
Reliable, in-order delivery
  Checksums to detect corrupted data
  Acknowledgments & retransmissions for reliable delivery
  Sequence numbers to detect losses and reorder data
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 73: TCP is a “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 0
Byte 1
Byte 2
Byte 3
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.

## Slide 74: Why do I need to broke a package into segments?
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes on an Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header is typically 20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 75: Sequence Numbers
Host A
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte
Why the ISN number cannot be zero?

## Slide 76: TCP Three-Way Handshake
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
Data
A
B
Data
Each host tells its ISN to the other host.

## Slide 77: TCP Three-Way Handshake
SYN=1, seq=A
A
B

## Slide 78: TCP Three-Way Handshake
SYN=1, seq=A
A
B
SYN=1 , seq=B, ACK=A+1

## Slide 79: TCP Three-Way Handshake
SYN=1, seq=A
A
B
SYN=1 , seq=B, ACK=A+1
seq=A+1, ACK=B+1

## Slide 80: Connection Termination

## Slide 81: TCP Retransmission (ARQ)
Automatic Repeat reQuest (ARQ)
Automatic Repeat Request
  Receiver sends acknowledgment (ACK) when it receives packet
  Sender waits for ACK and timeouts if it does not arrive within some time period
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 82: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS

## Slide 83: Why does require TCP Sliding Window?
Stop-and-wait is inefficient
  Only one TCP segment is “in flight” at a time
  Especially bad when delay-bandwidth product is high
Numerical example
  1.5 Mbps link with a 45 msec round-trip time (RTT)
    Delay-bandwidth product is 67.5 Kbits (or 8 KBytes)
  But, sender can send at most one packet per RTT
    Assuming a segment size of 1 KB (8 Kbits)
    … leads to 8 Kbits/segment / 45 msec/segment  182 Kbps
    That’s just one-eighth of the 1.5 Mbps link capacity

## Slide 84: Sliding Window
Window size
  Amount that can be sent without acknowledgment
  Receiver needs to be able to store this amount of data
Receiver advertises the window to the receiver
  Tells the receiver the amount of free space left
  … and the sender agrees not to exceed this amount
Client windows < server window
Segment = 1000 bytes

## Slide 85: TCP State-Machine

## Slide 86: Computational Intelligence (TC2027)